## Slide 1
20T hybrid block-coil
V5.5
E. Rochepault
22/08/2022

## Slide 2: Best case with field quality – 5.5
138 MPa
118 MPa
110 MPa
@ 20 T in the bore
No iron
Grading factor = 0.9
Quadrant area = 9000 mm2
bn [unit] | Matlab Analytical | Ansys No iron | Ansys iron
b3 | -6.27 | -6.33 | -0.55
b5 | -3.18 | -3.12 | -2.99
b7 | -0.131 | -0.088 | -0.065
b9 | 0.113 | 0.100 | 0.085
Without iron:

## Slide 3: Operating Points – 5.5
Without iron
With iron
 |  | Matlab | Ansys | Ansys
 |  | No iron | No iron | iron
20 T |  |  |  | 
JHF | A/mm2 | 343.4 | 343.7 | 317.0
JLF | A/mm2 | 309.1 | 309.3 | 285.3
B0 | T | 19.99 | 20.00 | 20.00
Bpeak,HF | T | 20.75 | 20.76 | 20.76
Bpeak,LF | T | 15.46 | 15.47 | 15.77
Margin | % | 15.5 | 15.4 | 16.5
Sx peak LF | MPa | 118.4 | 117.3 | 109.7
Sx peak HF | MPa | 138.6 | 140.3 | 142.0
Sy peak | MPa | 110.5 | 110.6 | 89.6
Short sample |  |  |  | 
JHF,SS | A/mm2 | 406.1 | 406.4 | 379.6
JLF,SS | A/mm2 | 365.5 | 365.7 | 341.6
B0,SS | T | 23.65 | 23.65 | 23.66
BSS,HF | T | 24.54 | 24.55 | 24.55
BSS,LF | T | 18.3 | 18.30 | 18.60
Sx peak LF | MPa | 165.5 | 164.1 | 155.0
Sx peak HF | MPa | 193.7 | 196.2 | 201.2
Sy peak | MPa | 154.4 | 154.7 | 126.6

## Slide 4: Rigid boundaries
Fixed nodes everywhere but the coil blocks
Lorentz forces only
With iron
 Same as analytical model
143 MPa
108 MPa
86 MPa
Sx
Sy

## Slide 5: Bonded components
All surrounding components bonded
 High peak stresses in corners
228 MPa
725 MPa
668 MPa
Sx
Sy
179 MPa

## Slide 6: Free components
All surrounding components free (separation + sliding)
 No stress decoupling, peak in corner
265 MPa
116 MPa
Sx
Sy
167 MPa

## Slide 7: Bonded components – 10 mm structure
Ribs and plate 10 mm thick
Current calculated to generate the same peak stress
 No significant improvement
~230 MPa
713 MPa
652 MPa
Sx
Sy
~170 MPa

## Slide 8: Sliding cage
Vertical plates free to slide
BC ux=0 realeased
 Slight decrease of peak stresses
~230 MPa
556 MPa
504 MPa
Sx
Sy
~140 MPa

## Slide 9: Detached ribs
Ribs in ‘rough’ contact
= separation but no sliding
 Slight decrease of peak stresses
~210 MPa
673 MPa
635 MPa
Sx
Sy
~140 MPa

## Slide 10: Preload
“Conceptual preload” = External pressure on the rails to “counter-bend” the ribs
 No significant improvement
764 MPa
140 MPa
Sx at preload
Sx at nominal
219 MPa
150 MPa
75 MPa
427 MPa

## Slide 11: Soft insulation – to be calculated
Coil blocks surrounded by a soft layer of insulation
 Likely to decrease locally the peak stresses
Sx
Sy

## Slide 12: Taking into account plasticization – to be calculated
Bi-linear model for coil blocks Taking into account plasticization
 Likely to decrease locally the peak stresses, but non predictable effect of a higher deformation

## Slide 13: Taking into account plasticization – to be calculated
Bi-linear model for coil blocks Taking into account plasticization
 Likely to decrease locally the peak stresses, but non predictable effect of a higher deformation

## Slide 14: Adding stress-release in components
Adding notches or springs in components to absorb deformation
 Likely to decrease locally the peak stresses, but requires a more advanced engineering design