## Slide 1: Object Detection and Tracking, Source Object Attribution, and Application in Sensor Networks
Ren Cooper
Lawrence Berkeley National Laboratory
Radiological Data Fusion Workshop
August 15th, 2023
RJCooper@lbl.gov

## Slide 2: Outline
Radiological Source Object Attribution
Application to City-scale Networked R/N Detection
Research Needs

## Slide 3: Motivation
Contextual information allows us to measure/quantify the factors that influence the measurements we make with radiation detectors
This helps to inform and/or constrain the inversion from measured counts to actionable information
When the detector is moving, we track its motion and the environment it is moving through
When the detector is stationary, we measure the world around it
E.g. tracking objects that could be carrying a source
Leverage inverse square law to provide localization and situational awareness
Improve detection sensitivity by optimizing integration time
E.g., presence, nature, strength location of an anomaly

## Slide 4: Motivation
Contextual information allows us to measure/quantify the factors that influence the measurements we make with radiation detectors
This helps to inform and/or constrain the inversion from measured counts to actionable information
When the detector is moving, we track its motion and the environment it is moving through
When the detector is stationary, we measure the world around it
E.g. tracking objects that could be carrying a source
Leverage inverse square law to provide localization and situational awareness
Improve detection sensitivity by optimizing integration time
E.g., presence, nature, strength location of an anomaly
Disclaimer: We are not the first to leverage object tracking for radiation detection (e.g. Roadside Tracker) but we are now doing it in 3D, in real-time, and in ~complex or unconstrained environments

## Slide 5: Static ”SDF” Systems
Fixed Installation
Compact, redeployable
40 cm

## Slide 6: Methodology
M.R. Marshall et al., IEEE TNS(2020), DOI: 10.1109/TNS.2020.3047646
Image Frame
Acquire Video and/or Lidar Data in Real Time

## Slide 7: Methodology
M.R. Marshall et al., IEEE TNS(2020), DOI: 10.1109/TNS.2020.3047646
Detect and Classify Objects
(Return positions)
Object
Detection
CNN
Image Frame
Obj. Positions

## Slide 8: Methodology
M.R. Marshall et al., IEEE TNS(2020), DOI: 10.1109/TNS.2020.3047646
Object
Detection
CNN
Image Frame
Kalman
Filter
Tracker
Obj. Positions
Tracks
Track Objects in 3D

## Slide 9: Methodology
M.R. Marshall et al., IEEE TNS(2020), DOI: 10.1109/TNS.2020.3047646
Object
Detection
CNN
Image Frame
Kalman
Filter
Tracker
Obj. Positions
Tracks
Rad Data
Poisson
Attribution
Attribution
Spectral Alarm
Detection
Upon alarm:
Build track-informed model of time-series peak count rate for each object
Fit tracks to data (maximize Poisson likelihood)
Compute “exclusion metrics” e.g. p-value or s-value
Video
Lidar

## Slide 10: Video vs. Lidar
Video | Lidar
Information rich | Direct 3D object detection
Human interpretable | Long range
Wealth of open-source detection models | Works in adverse conditions/at night
Depth must be inferred | Performance might degrade in heavy rain
Limited range | Limited object detection models
Doesn’t work at night | Reflections can degrade performance
We have so far observed superior source-object attribution performance when using Lidar
  In a mock urban environment: 80% correct attribution Lidar vs. 60% video

## Slide 11: Video vs. Lidar
Video | Lidar
Information rich | Direct 3D object detection
Human interpretable | Long range
Wealth of open-source detection models | Works in adverse conditions/at night
Depth must be inferred | Performance might degrade in heavy rain
Limited range | Limited object detection models
Doesn’t work at night | Reflections can degrade performance
We have so far observed superior source-object attribution performance when using Lidar
  In a mock urban environment: 80% correct attribution Lidar vs. 60% video
We should explore other sensors - Stereo cameras? Acoustic sensors? Radar?

## Slide 12: PANDAWN Network
The PANDA and DAWN projects are establishing a city-scale, multi-sensor testbed for networked radiological/nuclear detection
PANDA–DAWN key features:
Contextual sensor integration
Adaptive algorithms
Data fusion
Enabled by:
Edge and cloud computing
Inter-node communication
Achieving:
Improved source detection performance
Increased domain awareness
  Inc. source localization and tracking
Increased flexibility and stability
Rich data sets for algorithm development
Exiting nodes
hospital region
Downtown Grid
Major Intersection
River-crossing grid

## Slide 13: Visual Object Detection Observations From the Field
Real-world object detection performance is very good using YOLOv7-tiny and pre-trained model
Performance falls away at distances > 30 m
Some degradation in poor conditions may be improved with updated training
Tracking and attribution performance TBD
Estimated Distance (m)
Performance Metric
Precision
Recall
Accuracy
False Negatives

## Slide 14: Network Data Fusion
Simulations show the potential for networked detection to outperform conventional detection
  Increased sensitivity to weak sources
  Reduced false positive rates
  Reduced detector density
Contextual information is required to identify correlated observations in a sparse network
  Vehicle make/model/color, license plate etc.
5 mCi 137Cs source, FAR = 1/8 hours

## Slide 15: (Some) Research Needs
Detailed characterization of performance (coming soon…)
Understanding of optimum detector choice for a given CONOP
Comprehensive study of contextual sensor trade-offs?
  What about the fusion of multiple sensors?
  Depth-extracting CNNs for video?
Methods to more fully account for attenuation
  In scene, between tracked objects, and within tracked objects
  Better physics model  more well bounded statistical metrics
Use of full spectral information rather than peak counts
Can we apply scene-dependent background models?
Network-level:
  Extraction of object characteristics
  Object re-detection networks
  Other methods to identify and track specific objects

## Slide 16
Thank You!
Photo Credit: Mark Bandstra, ANP
Funding: DOE NSSA NA22, DOE NNSA NA84, DHS CWMD, DTRA
Acknowledgements: Nico Abgralla, G. Aversanoa, Mark Bandstraa, Xin Chena, Dan Hellfelda, Tenzing Joshia, Matt Marshalla,b,Victor Neguta, Brian Quitera, Marco Salathea, Kai Vettera,b, Pete Beckmanc, Charlie Catlettc, Yongho Kimc, Raj Sankaranc, Sean Shahkaramic
a Lawrence Berkeley National Laboratory
b University of California, Berkeley
c Argonne National Laboratory

## Slide 17: Optimization of Integration Time

## Slide 18: Pattern-of-Life Analysis and Predictive Analytics