## Slide 1
Data-Driven Autonomous Radiation Source Search
DRAG RDF22
Radiological Data Fusion (RDF) Workshop 2023
Berkeley, 15-16 August 2023
Emil Rofors, Mark S. Bandstra, Daniel Hellfeld, Tenzing H.Y. Joshi, Alex Moran, Marco Salathe, Jayson R. Vavrek, Kai Vetter, Brian J. Quiter
Applied Nuclear Physics, LBL
Notes: 1

## Slide 2
Outline
Autonomy scale
Path-planning
Behavior trees for autonomy
SDF & autonomy
SDF Concept: R Barnowski et al., “Scene data fusion: Real-time standoff volumetric gamma-ray imaging,” NIM A, 800, 65–69 (2015).
First SFD examples: A Haefner et al., “Handheld real-time volumetric 3-d gamma-ray imaging,” NIM A, 857, 42–49 (2017).
Origins of SDF – handheld qualitative gamma-ray imaging
2021-2022: Quantitative SDF at km scales using a variety of platforms
Notes: Scene data fusion is

## Slide 3
Manual
Portable
Cost-effective
Remote-controlled
Lower exposure
Hard-to-reach areas
Autonomy-scale
Less human interaction
Pre-programmed
Consistency
Coverage
Cs137
Autonomy
Simple
Speed

## Slide 4
Generate gridded flight paths for manually drawn shapes
Boustrophedon pattern (lawn mower)
Based on https://github.com/18alantom/CoveragePathPlanning
Downsample shape to grid-sized pixels
Calculate coverage pattern
Path planning 2D coverage
Draw region on map
Run for all angles
Select shortest solution
Notes: time per calculation
can add and account for obstructions online

## Slide 5
Kromek Sigma50,
CsI(Tl) 1x1x2”3 (300 grams)
Autonomous system used
Intel NUC running Ubuntu
Theiss hexacopter
Up to 12 lb payload
~20 min flight time
Source: 1.4 mCi Cs137
Autonomy behaviour:
Pre-program a grid
Prioritize suspected sources
Skier searching after an avalanche
Notes: cross to maximize 1/r2 information

## Slide 6
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 7
Take off
Scan area
SDF & Autonomy
Return home
Sequence, move to next if child succeeds
Text
Action, do something
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 8
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
Sequence, only does next if previous succeed
Text
Action, do something
Scan area
Return home
Return home
arm
liftoff
Text
Action, do something
Sequence, move to next if child succeeds
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 9
Selector, move to next if child succeeds or fails
Scan area
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
Return home
?
Return home
Battery low
arm
liftoff
Text
Condition, true or false
returns success or fail
Text
Action, do something
?
Sequence, move to next if child succeeds
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 10
Selector, move to next if child succeeds or fails
Scan area
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
Return home
?
Return home
Battery low
arm
liftoff
Text
Condition, true or false
returns success or fail
Text
Action, do something
?
Sequence, move to next if child succeeds
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 11
Selector, move to next if child succeeds or fails
Scan area
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
Return home
?
Return home
Battery low
arm
liftoff
Text
Condition, true or false
returns success or fail
Text
Action, do something
?
Sequence, move to next if child succeeds
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 12
Selector, move to next if child succeeds or fails
Scan area
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
Return home
?
Return home
Battery low
arm
liftoff
Text
Condition, true or false
returns success or fail
Text
Action, do something
?
Sequence, move to next if child succeeds
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 13
Selector, move to next if child succeeds or fails
Scan area
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
Return home
?
Return home
Battery low
arm
liftoff
Text
Condition, true or false
returns success or fail
Text
Action, do something
?
Sequence, move to next if child succeeds
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 14
Selector, move to next if child succeeds or fails
Scan area
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
Return home
?
Return home
Battery low
arm
liftoff
Text
Condition, true or false
returns success or fail
Text
Action, do something
?
Sequence, move to next if child succeeds
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 15
Selector, move to next if child succeeds or fails
Scan area
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
Return home
?
Return home
Battery low
arm
liftoff
Text
Condition, true or false
returns success or fail
Text
Action, do something
?
Sequence, move to next if child succeeds
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 16
Selector, move to next if child succeeds or fails
Scan area
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
Return home
?
Return home
Battery low
arm
liftoff
Text
Condition, true or false
returns success or fail
Text
Action, do something
?
Sequence, move to next if child succeeds
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 17
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
Return home
?
Return home
Battery low
arm
liftoff
Sequence, only does next if previous succeed
Selector, tries one by one, even on fail
Text
Condition, true or false
returns success or fail
Text
Action, do something
?
?
Return home
Battery low
Follow raster
arm
liftoff
Selector, move to next if child succeeds or fails
Text
Condition, true or false
returns success or fail
Text
Action, do something
?
Sequence, move to next if child succeeds
Go check any suspected source
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 18
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
Return home
?
Return home
Battery low
arm
liftoff
Sequence, only does next if previous succeed
Selector, tries one by one, even on fail
Text
Condition, true or false
returns success or fail
Text
Action, do something
?
?
Return home
Battery low
Go to unidentified source
Go down and fly X-pattern
Follow raster
arm
liftoff
No suspected sources
?
Selector, move to next if child succeeds or fails
Text
Condition, true or false
returns success or fail
Text
Action, do something
?
Sequence, move to next if child succeeds
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 19
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
Return home
?
Return home
Battery low
arm
liftoff
?
Return home
Battery low
Go to unidentified source
Go down and fly X-pattern
Follow raster
arm
liftoff
No suspected sources
?
z-score
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 20
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
Return home
?
Return home
Battery low
arm
liftoff
?
Return home
Battery low
Go to unidentified source
Go down and fly X-pattern
Follow raster
arm
liftoff
No suspected sources
?
z-score
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 21
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
Return home
?
Return home
Battery low
arm
liftoff
?
Return home
Battery low
Go to unidentified source
Go down and fly X-pattern
Follow raster
arm
liftoff
No suspected sources
?
z-score
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 22
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
Return home
?
Return home
Battery low
arm
liftoff
?
Return home
Battery low
Go to unidentified source
Go down and fly X-pattern
Follow raster
arm
liftoff
No suspected sources
?
z-score
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 23
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
z-score
Return home
?
Return home
Battery low
arm
liftoff
?
Return home
Battery low
Go to unidentified source
Go down and fly X-pattern
Follow raster
arm
liftoff
No suspected sources
?
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 24
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
z-score
Return home
?
Return home
Battery low
arm
liftoff
?
Return home
Battery low
Go to unidentified source
Go down and fly X-pattern
Follow raster
arm
liftoff
No suspected sources
?
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 25
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
z-score
Return home
?
Return home
Battery low
arm
liftoff
?
Return home
Battery low
Go to unidentified source
Go down and fly X-pattern
Follow raster
arm
liftoff
No suspected sources
?
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 26
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
z-score
Return home
?
Return home
Battery low
arm
liftoff
?
Return home
Battery low
Go to unidentified source
Go down and fly X-pattern
Follow raster
arm
liftoff
No suspected sources
?
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 27
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
z-score
Return home
?
Return home
Battery low
arm
liftoff
?
Return home
Battery low
Go to unidentified source
Go down and fly X-pattern
Follow raster
arm
liftoff
No suspected sources
?
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 28
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
z-score
Return home
?
Return home
Battery low
arm
liftoff
?
Return home
Battery low
Go to unidentified source
Go down and fly X-pattern
Follow raster
arm
liftoff
No suspected sources
?
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 29
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
z-score
Return home
?
Return home
Battery low
arm
liftoff
?
Return home
Battery low
Go to unidentified source
Go down and fly X-pattern
Follow raster
arm
liftoff
No suspected sources
?
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 30
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
z-score
Return home
?
Return home
Battery low
arm
liftoff
?
Return home
Battery low
Go to unidentified source
Go down and fly X-pattern
Follow raster
arm
liftoff
No suspected sources
?
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 31
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
z-score
Return home
?
Return home
Battery low
arm
liftoff
?
Return home
Battery low
Go to unidentified source
Go down and fly X-pattern
Follow raster
arm
liftoff
No suspected sources
?
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 32
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
z-score
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 33
SDF & Autonomy
LAMP detector payload communicating with UAV
Instructed to fly in grid, prioritize any source found on the way
Logic implemented via a behaviour tree
z-score
Future work
Mission-tailored behaviors
Multiple sources
Distributed sources
MDA-minimization
Contour mapping
Algorithms at different update frequency in parallel
Notes: Now that we have all this quantitative information about the surroundings in real-time we can use that to guide robots. We then have the ability if there seems to be a source over there say to a drone - go fly over there and if that estimation changes as it moves it’s very fast to rethink its path.

## Slide 34
Simulated autonomy
Gazebo environment
Photo from flight
Full real-time simulation
Test-bench for behaviors before real flights

## Slide 35
Simulated autonomy
Microsoft Airsim in Unreal Engine
Radiation source search game, 2023
Game engines offer realistic, interactive worlds for simulations
Ground truth segmentation, LIDAR, radiation et. c. available

## Slide 36
Tell the robot:
Look under that bridge
Follow the pipe
Follow him with the hat
The robot communicates with the operator:
The area is cleared
Suspected source by the house, need to go closer.
Emerging capabilities with large language models (LLMs)
https://aka.ms/ChatGPT-Robotics

## Slide 37
Tell the robot:
Look under that bridge
Follow him with the hat
The robot communicates with the operator:
The area is cleared
Suspected source by the house, need to go closer.
Emerging capabilities with large language models (LLMs)
https://aka.ms/ChatGPT-Robotics

## Slide 38
Conclusions
Autonomy developing hand-in-hand with SDF.
Real-time running SDF enables responsive autonomy
  Faster localization
  Efficient use of battery / time
  Lower MDA / larger area covered
Behaviour tree design is versatile and simple for autonomy
Simulations developed that can test new functions and speed-up development
Future work span beyond source search shown here
Notes: Look up NNSA

## Slide 39
Acknowledgments & Disclaimer
This work was performed under the auspices of the U.S. Department of Energy by Lawrence Berkeley National Laboratory under Contract DE-AC02-05CH11231 funded by the U.S. Department of Energy/National Nuclear Security Administration’s (DOE/NNSA’s) Office of Defense Nuclear Nonproliferation R&D (DNN R&D) and in support of the DNN R&D-supported Consortium for Enabling Technologies and Innovation (ETI).
The point source likelihood algorithm development was supported by the Defense Threat Reduction Agency under HDTRA 10027- 21370, 10027- 28018, 10027- 30529, 10027- 23334, 10027-28546, 10027- 28022. This support does not constitute an express or implied endorsement on the part of the United States Government.

## Slide 40
Thank you! Questions?
40
Contact: erofors@lbl.gov

## Slide 43
Return home
?
Return home
Battery low
arm
liftoff
?
Return home
Battery low
Go to unidentified source
Go down and fly X-pattern
Follow raster
arm
liftoff
No suspected sources
?