## Slide 1
Summary of the Annual International Muon Collider Collaboration Meeting
Steve Gourlay
19 July 2023

## Slide 2: Why a Muon Collider?
Muons are elementary particles – all their collision energy is used
  X7 mass reach compared to protons at the same energy
  More compact – less expensive – can fit on FNAL site
200 times heavier than electrons
  Negligible synchrotron radiation – energies to many TeV compared to 300 – 500 GeV for electrons
  Lower energy spread – higher precision
  Larger cross sections for certain interactions
And . . . some people living now may see it built and operated!

## Slide 3: Acknowledgment
Input based on presentations prepared/given by
Daniel Schulte, Roberto Losito, Lionel Quettier, Luca Bottura, Alfredo Portone, Marco Statera, Siara Sandra Fabbri, Bernardo Bordini, Carlotta Accettura, Marco Breschi, Fulvio Boattini, Barbara Caiffi, Samuele Mariotto, Stefania Farinon

## Slide 4: Project organization
The magnet work packages of IMCC and MuCol are in essence the same, with identical tasks and workplan.
Activities are followed-up mainly through the “muons magnets Working Group” (mmWG)
International Muon Collider Collaboration
MuCol EU Design Study

## Slide 5: MuCol Status and Goals
MuCol was created to coordinate the efforts of the International Muon Collider Collaboration towards the specific goal of providing comprehensive input for the next European Strategy for Particle Physics Update
The main deliverables will be yearly progress reports
  Basis for a report that will be submitted to the ESPPU in 2025/26 as input from the Collaboration.
MuCol proposal was submitted in April ‘22 and approved with an excellent evaluation.
The consortium includes 31 Institutes:
  CERN as coordinator and beneficiary
  11 more Beneficiaries (no UK Institutes)
  19 Associated Partners

## Slide 6: Accelerator R&D Roadmap
No insurmountable obstacles found for the muon collider
  BUT . . . Needs significant R&D
Aim at 10+ TeV with a potential initial stage at 3 TeV
Full scenario deliverables by next ESPPU/other processes
  Project Evaluation Report
  R&D Plan that describes a path toward the collider and allows informed decisions
  Interim report by end of 2023
Reduced scenario
  Significantly reduced scope and lacks most preparations for a demonstration program
Do not yet have the resources of the reduced scenario
  Are approaching ~ 40 – 50 FTE for the accelerator
  Looking for more

## Slide 7: Overarching theme of the meeting . . .
Cost, Performance and Sustainability

## Slide 8: Cost and Sustainability
Compactness promises cost effectiveness
And low CO2 footprint for construction
Increasing luminosity per beam power promises power efficiency
Staging is possible
Synergies exist (neutrino/higgs)
Unique opportunity for a high-energy, high-luminosity lepton collider
D. Schulte

## Slide 9: Staging
Ideally would like full energy right away, but
staging could lead to faster implementation
Substantially less cost for a first stage
Can make technical compromises
  e.g. 8 T Nb-Ti magnets would increase collider ring from 4.5 to 6 km and reduce luminosity by 25%
Timeline might be more consistent with human lifespan
Upgrade adds one more accelerator and new collider ring
only first collider ring is not being reused
D. Schulte

## Slide 10: Muon Collider magnet “specs”
Final Cooling solenoids
Field: > 40 T (ideally 60 T)
Bore: 50 mm
Length: ≈ 500 mm (x 17)
Radiation heat: TBD
Radiation dose: TBD
RCS
Target solenoids
Field: 20 T… 2T
Bore: 1200 mm
Length: 18 m
Radiation heat: ≈ 4.1 kW
Radiation dose: 80 MGy
Collider ring magnets
Field: 16 T peak (IR 20 T)
Bore: 150 mm
Length: 10 m … 15 m (x 700)
Radiation heat load: ≈ 5 W/m
Radiation dose: ≈ 20…40 MGy
Accelerator magnets
Field: ±1.8 T (NC), < 10 T (SC)
Rate: 400 Hz (NC), SS (SC)
Bore: 100 mm(H) x 30 mm(V)
Length: 3 m … 5 m (x 1500)
Radiation heat: ≈ 3 W/m
Radiation dose: TBD
6D Cooling solenoids
Field: 4 T … 19 T
Bore: 90 mm … 600 mm
Length: 1 km (x 2)
Radiation heat: TBD
Radiation dose: TBD
D. Schulte

## Slide 11: Muon Collider magnet “team”
CERN
INFN
CEA
CNRS PSI
UniGE
SO’TON
uniTwente
RCS
CERN
F4E (Barcelona)
F4E (Garching)
INFN
UniMI
CERN
TUT
CERN
UniBO
TUDa
UniTwente
INFN
CERN
UniMI
KIT
Task 7.2
Task 7.3
Task 7.4

## Slide 12: Target and Capture
MAGNET SPECS
Field: 20 T… 2T
Bore: 1200 mm
Length: 18 m
Radiation heat load: ≈ 4.1 kW
Radiation dose: 80 MGy

## Slide 13
Technology | Pro’s | Con’s
ALL Resistive | Known technology (TRL 9) | Large dimension and mass Very large electric power consumption o(100MW)
LTS + Resistive | Known technology (TRL 9) | Large dimension and mass Electric power consumption (10 MW)
LTS + HTS, Insulated | Known design principles Synergy with other fields of science application Can profit from development by others (e.g. NHMFL) | Large dimension and mass Developmental technology (TRL 6/7)
ALL HTS, Insulated | More compact than LTS/HTS Allows for operation at higher temperature | R&D at low readiness (TRL 4/5)
ALL HTS, Non-insulated | Most compact magnet winding Synergies with other fields of science and societal applications Can profit from development by others (e.g. NHMFL) | R&D at low readiness (TRL 3/4/5) Ramping time and field stability need to be demonstrated
Target and Capture: Magnet Technologies

## Slide 14
US-MAP
Proposal
EM = 2.9 GJ
Top = 4.2 K
Mcoils = 200 tons
Mshield = 300 tons
P = 12 MW
EM = 1 GJ
Top = 10…20 K
Mcoils = 110 tons
Mshield = 196 tons
P = 1MW
Remove resistive insert (10 MW), HTS to achieve field of 20 T
Reduce shield thicknes, accepting higher heat load at 20 K
Field profile matches the requirements from beam optics
Target and Capture: Magnet specifications

## Slide 15: Target and Capture Design Considerations
Main design drivers are power consumption and heat deposition
Hybrid US-MAP (5 resistive coils and 19 SC coils, 2.4 m bore ) OR
Alternative - All HTS, 1.2 m bore  and operating at 10 – 20K
Strong synergy with requirements on magnets for tokamak nuclear fusion devices
  Central Solenoid Coils: Higher Bop higher flux  higher reactor availability factor
  Toroidal Field Coils: Higher Top larger acceptable heat load  compact shielding  cost

## Slide 16
VIPER-like cable (HTS tapes, central cooling hole, steel jacket) with Imax61 kA
Set of 23 coils in 3 sections (300 mm gap between sections, 20 mm gap between coils)
Peak field B=20.9 T, magnetic energy 1.1 GJ, cable length  8.7 km, winding mass  115 t
Field on axis within 4% accuracy of Sayed-Berg formula over 16 m channel length
Stresses in structural elements within 316 LN limits (sY 1000 MPa)
Stresses in tapes being investigated to be minimized (txy30 MPa)
Coils operating at 20 K, 20 bar, 15 W pumping power, 150 W heat removal
High conductor stability (DT≥10 K!)
Detection & dump for quenches in low field/current most challenging (long detection times) but seems compatible with hot-spot temperature limit (THS  150-200 K)
Target and Capture: Magnet Design Highlights

## Slide 17: 6D Cooling
6D Cooling solenoids
Field: 4 T … 19 T
Bore: 90 mm … 600 mm
Length: 1 km (x 2)
Radiation heat: TBD
Radiation dose: TBD

## Slide 18: Cooling Channel
Full list based on original US MAP design (field on axis)
12 unique stages:
  4 cooling stages before bunch recombination (A1-A4)
  8 cooling stages after bunch recombination (B1-B8)
Each stage has a repeating series of a cell type
High field, very compact solenoids
Each cell has symmetric solenoids of opposite polarity
Some stats:
Fields on axis: 2 to 14 T
Cell Lengths: 0.8 to 2.7 m
Total length of all Stages: ~ 1 km
Total number of solenoids: 2432
NbTi
Nb3Sn
HTS
By S. Fabbri and J. Pavan

## Slide 19: Technologies within cells
By S. Fabbri
Three technologies at lower temperature (4 K) or one technology at 20 K

## Slide 20: To be investigated
We are defining technologies
Conductor
Operating conditions, i.e. temperature and cooling method
To be investigated
Conductor performance
Conductor configuration
Field quality
Thermal/mechanical configuration

## Slide 21: Technologies 6D cooling solenoids
Technology | Pro’s | Con’s
LTS | Known technology (TRL 9) | Operating temperature
HTS ReBCCO Insulated | More compact than LTS/HTS Allows for operation at higher temperature Batch above 100 m demonstrated | R&D at low readiness (TRL 4/5) Quench detection protection Production of km batches to be demostrated
HTS ReBCCO Non-insulated | Most compact magnet winding Synergies with other fields of science and societal applications Batch above 100 m demonstrated Can profit from development by others (e.g. NHMFL) | R&D at low readiness (TRL 3/4/5) Ramping time and field stability need to be demonstrated Quench detection and protection Production of km batches to be demostrated
HTS BiSSCO/IBS | Round wire demonstrated for BiSSCO | R&D at low readiness (TRL 3/4) for IBS Production lengths (?)

## Slide 22: Muon Collider magnet “team”
CERN-EP
  Contribution to development of HTS technology for UHF solenoids
  Contact person: A. Dudarev
  Baseline studies for HF solenoids
  Engineering design
  R&D pancakes
PSI
  Contribution to target and cooling solenoids design and technology R&D
    Instrumentation and analysis of NI coils (in synergy with other projects that provide the coils)
    Powered samples to test mechanical limitations (NOTE: need to brainstorm)
    Integrated conceptual target-magnet design, in close iteration loops with particle-shower simulations
  Contact person: Dr. B. Auchmann
  Instrumentation for test coils (vtap, protection schemes and devices)
  R&D pancakes
University of Geneva
  Measurements in support to R&D on HTS
    Electro-Mechanical characterization and limits at high field (NOTE: need to brainstorm)
  Contact person: Prof. C. Senatore
  Characterization measurements and conductor review
INFN LASA
  Critical current measurement
  Contact person: Dr. Marco Statera
  Coordination
  Define reference geometries fo r small coils (L. Bottura)
  Design of test coils devices (together with CERN, CEA…)
  R&D pancakes
  Test of small coils
University of Southampton
  Design of solenoids and measurement of HTS properties
  Test in background field (10 T, 110 mm)
  Contact person: Prof. Y. Yang
  Review of material options REBCO, Bi-2212, Bi-2223, IBS
  Evaluate current distribution in multi tape windings
  Mechanical and electro-mechanical properties
  R&D pancakes
  Test of small coils
University of Twente
  Contribute to the design and conductor effort
    HTS conductor design (both ReBCO and B2223) at the level of basic strand/tape, shape optimization and reinforcements
    HTS smart innovative cabling to allow for higher current, current sharing redundancy and quench protection
    HTS conductor characterization/review for limiting strain and cycling degradation
    HTS coil windings with controlled resistance to smartly balance conflicting requirements of ramp loss and quench stability
  Contact person: Prof. A. Kario
  Mechanical and electro-mechanical properties
KIT
  R&D on coils and tests
  Contact person: Dr T. Arndt
  Test coils winding and test, model development

## Slide 23: Ongoing activities
Tape characterization
Preliminary design of coils and cell
  Design of a HTS dipole for IRIS, Next Gen EU
  Winding tests of small pancakes
  Test of small pancakes (also in field)
  Design of the RF test station (in collaboration with WP8)
Coil design for the cells
  Field and forces
  Integration of cooling system
  Field quality definition and optimization

## Slide 24: Test coils
Test coils Identical/similar configurations used at CERN, INFN, PSI
Geometry
Configuration
Tests self field and in field
Validate handling procedures and models
60 mm inner diameter
20 mm and 60 mm thickness
4 mm and 12 mm tape width
Single and double pancakes winding
One- and two-in-hand winding
Pancakes can be stacked in mini-coils
By S. Sorti

## Slide 25: Conductor configurations
Explore the Controlled-Insulation vs non-insulation solutions.
Multi-tape winding is foreseen, including different materials and technologies to impact the inter-turn resistance.
The goal of this campaign is to asses and improve the TRL of such technologies in magnet-like conditions.
Examples of target technologies: Metal-Insulated (MI), multi-tape NI, multi-tape resistive layer + stabilizer.
HTS
Cu
substrate
metal
metal
High RRR

## Slide 26: Test of small coils
Synergies with IRIS (NextGenerationEU)
  Operation at T in the range 10 K – 30 K;
  Induction of flux densities in the tesla range
  Test in field up to 20+ T
  Non-round geometries (PNRR-IRIS project)
The goal is to test magnet-like conditions for NI coils and further validate models.
Target time: begin 2024
Coils are tested in CERN, INFN LASA, PSI, LNCMI, CEA
Draft of Variable Temperature system for small coils test

## Slide 27: RF test station
Select and validate a technology and design options
Design and commission a real size cell-like magnetic system
Synergy between two WPs
600 mm RT bore for RF
7 T (to 10 T)
+- 5 Tons range forces
SC HTS coils
Two stage
cryocooler
Vacuum vessel
Coil support structure
Tie rods for repulsion and compression forces
Thermal shield
RF cavity
Sc magnet/cryostat sketch by M. Castoldi & Stefano Sorti, UMIL & INFN-LASA
(RF drawing by Guillaume Ferrand –CEA

## Slide 28: Conclusion
An overview of the required coils
  12 cells
  18 different coils
  1 km of 6D cooling
We set the driving parameters and the technology we are aiming to
A full R&D program for tape characterization and conductor development
Focus on modeling (magnetization, current distribution…)
Many synergies in the project and in other applications
Performance-Cost-Sustainability together with compatibility with series production

## Slide 29: Final Cooling Channel
Final Cooling solenoids
Field: > 40 T (ideally 60 T)
Bore: 50 mm
Length: ≈ 500 mm (x 17)
Radiation heat: TBD
Radiation dose: TBD

## Slide 30: Ionizing Cooling Cell
16 Cells (MAP)
  Set of eight superconducting coaxial coils
  Peak field of 50T, 50 mm diameter
  Sayed et al. Phys. Rev. ST Accel. Beams 18, 091001
14 Cells (CERN)
  B > 40T, 50 mm diameter
R. Palmer, BNL
3.5 T

## Slide 31: Not exactly starting from scratch on high field solenoids – but . . .
Cross section of 45 T, 32 mm NHFML user facility solenoid
Hybrid Magnet 33.5 T from resistive insert, 11.5 T by superconducting outsert
30 MW power comsumption
https://nationalmaglab.org/user-facilities/dc-field/magnets-instruments/
Cross section of 36 T, 48 mm NHFML user facility (NMR) solenoid
Hybrid Magnet 23 T from resistive insert, 13 T by superconducting Nb3Sn CICC outsert
14 MW power comsumption
Cross section of 40*/37 T, 32/50 mm CHMFL user facility solenoid
Hybrid Magnet 29/26 T from resistive insert, 11 T by superconducting Nb3Sn CICC outsert
20 MW power comsumption
http://english.hmfl.cas.cn/uf/ms/202202/t20220224_301451.html
B. Bordini, CERN

## Slide 32: Getting closer
Cross section of 32 T (15 T LTS, 17 T two ReBCO double pancake coils), 32 mm user facility solenoid https://nationalmaglab.org/user-facilities/dc-field/magnets-instruments/
Just increase the field and bore
Operate REBCO coils at 20K?
And then the 40T
But will nested coils work for MC?
Low J, mechanical challenges, QP
B. Bordini, CERN

## Slide 33: CERN approach
Single coil, high Je
  40T, 50 mm bore
Need higher field – but higher tensile radial stress
Apply precompression to all-HTS NI/MI single coil.
High potential for future particle accelerators and other societal applications
Substantial progress on design
Challenges
  High stresses
  Magnet protection – transients to control
  Charging time
Sunam NI one-body ReBCO magnet
26.4 T in 35 mm, J central pancake 404 A mm-2 (26.4 T HTS multi-width)
overall diameter and height: 172 and 327 mm
S. Yoon et al. Supercond. Sci. Technol. 29 (2016) 04LT04
B. Bordini, CERN

## Slide 34: Accelerator Ring
Accelerator magnets
Field: ±1.8 T (NC), < 10 T (SC)
Rate: 400 Hz (NC), SS (SC)
Bore: 100 mm(H) x 30 mm(V)
Length: 3 m … 5 m (x 1500)
Radiation heat: ≈ 3 W/m
Radiation dose: TBD

## Slide 35: Critical systems and main- specifications
The powering system is very interlinked with the resistive magnets design
The key performance drivers are directly related to the total energy and power to be delivered to the magnets, but also to the tracking accuracy that will have to be guaranteed.
This input should come from the beam studies
F. Boattini

## Slide 36: Fast-ramping Magnets
Rectangular magnet bore 100 mm x 30 mm
5.07 kJ/m
5.65…7.14 kJ/m
5.89 kJ/m
Main challenge is management of the power in the resistive dipoles (several tens of GW):
Minimum stored magnetic energy
Highly efficient energy storage and recovery
HTS flat racetracks
Simple HTS racetrack dipole could match the beam requirements and aperture
F. Boattini et al.
Full wave resonance
Commutated resonance (new)
Differerent power converter options investigated
1.8T RC with 10T SC

## Slide 37: Collider Magnets
Collider ring magnets
Field: 16 T peak (IR 20 T)
Bore: 150 mm
Length: 10 m … 15 m (x 700)
Radiation heat load: ≈ 5 W/m
Radiation dose: ≈ 20…40 MGy
10 TeV Option

## Slide 38: Working Group
INFN Milano
S. Mariotto, M. Statera, M. Prioli, E. De Matteis, R. Valente, S. Sorti
INFN Genova
B. Caiffi, A. Bersani, S. Farinon, D. Novelli
CERN
L. Bottura, A. Lechner
Tampere University
T. Salmi

## Slide 39: Heat Load and Radiation
Input by other studies:
Calculations of the heat load on magnet coils
Use of a W shielding (2-4 cm thick)
Considered 3 TeV and 10 TeV config
Results:
Power penetrating shield: 5W/m
Cumulative dose equal to 20-40 MGy in 10 years of operation
DPA max 1.3E-4 after 10 years
Shield thickness 4 cm to limit cumulative dose
Courtesy of
Anton Lechner
See “Shielding design and requirements”
A. Lachner, https://indico.cern.ch/event/1183573

## Slide 40: Radial Build-up
Beam aperture (5σ) 23.5 mm radius
Cu layer beam screen 0.01 mm thick
Tungsten absorber 40 mm thick
Thermal insulation 11 mm thick
Cold bore 3 mm thick
Coil pack 50 mm thick
Cryogenic options calculated using same assumption of heat load calculations
Tabsorber
Tcoil
Welett
Heavily dependent from geometry and heat loads
How to share last update designs?
Radial Building
Courtesy of Patricia Borges De Sousa
See “Cryogenics options for future accelerators”
Patricia Borges De Sousa, https://indico.cern.ch/event/1240043

## Slide 41: Material Options
Technology |  | Pro’s | Con’s
LTS (Nb-Ti) |  | Known and well developed technology (TRL 8) | Probably do not meet all magnet requirements
LTS (Nb3Sn) |  | Known technology, reaching demonstration level in accelerators (TRL 6/7) | Probably do not meet all magnet requirements Brittle/stress limited
Hybrid (LTS Nb3Sn) + (HTS) |  | Lower cost Exploit potential of both materials | Low readiness level for HTS insert (TRL 3/4) LTS/HTS joints and integration to be developed Temperature limited by LTS
All-SC (HTS) | Insulated | Most compact solution Allows operation at high temperature Profit from on-going R&D activities on insulation/no-insulation windings | R&D at low readiness (TRL 3/4) Quench protection to be demonstrated Field delay and field stability in case of NI winding
 | Controlled Insulated |  | 
 | Non Insulated |  | 

## Slide 42: Design Options (1/2)
Technology | Pro’s | Con’s
Cos-theta Design | Well known design Wound around a cylindrical mandrel, end shape already suitable for beam tube insertion | Mechanical structure can be complex Not most easy winding geometry for HTS tapes
Block Coil Design | Known design principles Mechanical structure simplify stress management Easier geometry for HTS-tapes | Difficult stress management on coil ends Higher ratio conductor length/produced field
Canted Cos-theta Design | Intrinsic stress management Low number of parts and tools Easy winding procedure | Requires more cable than the other layouts Quench protection more difficult R&D needed

## Slide 43: Design Options (2/2) Combined function
Technology | Pro’s | Con’s
NESTED Configuration | Separate Powering Dipole/Quadrupole Inherit experience on Nb3Sn magnets for HiLumi and LARP-US development program | High Stress on Internal Coil Alignment Higher Costs
Asymmetric Coil Design | Single type of coil Optimized margin and field quality | Fixed Dipole/Quadrupole ratio Stress on the supporting structure is not balanced
A. Zlobin
T. Ogitsu
Fields for 3 TeV are high, but 10 TeV very high!
Important negotiation point with machine designers

## Slide 44: Synergies
Huge help and feedback will come from:
20T+ development program in the US
CERN – HFM
Possible feedback loop also inside INFN
PNRR-IRIS project (see L. Balconi 20-05-2023) and small HTS coil pancake program
10 T of dipolar field
Bore dimensions 80x50 mm2
Operating temperature 20 K
Physical L < 1 m
Courtesy of
Jose Luis Rudeiros

## Slide 45: Cooling Options for the collider ring

## Slide 46: Updated radial build for collider arc magnets
Radial build has evolved to include a heat intercept between the absorber and the coil
Beam aperture (5σ) 23.5 mm radius
Cu layer beam screen 0.01 mm thick
Tungsten absorber 40 mm thick
Insulation space 5 mm thick
Heat intercept 1 mm thick
Insulation space 5 mm thick
Beam pipe 3 mm thick
Kapton insulation 0.5 mm thick
Clearance 1 mm thick
Coil pack* (60 mm thick) *thickness TBD, placeholder
Coil aperture 158 mm
P. Borges de Sousa

## Slide 47: Updated radial build for collider arc magnets
Radial build has evolved to include a heat intercept between the absorber and the coil
Baseline for heat load estimation/power consumption is 10 TeV machine
Source: Informal meeting on muon collider absorber, vacuum and cryogenics integration (18 January 2023) · Indico (cern.ch)
To cold mass
To absorber
From muon decay; total heat load will include substantial contributions, e.g. conduction, thermal radiation…
P. Borges de Sousa

## Slide 48: Power Consumption with heat intercept
Power consumption estimated for shown heat loads at various coil and absorber temperatures
48
Target: 25 MW for Cryo in collider
(2.5 kWel/m)
Message: 25 MW total for 10 km collider ring →
≥ 4.5 K
≥ 200 K
Shown: Cooling effort at refrigerator I/F, absorber thickness 4 cm, shield and heat intercept 80 K
P. Borges de Sousa

## Slide 49: Considerations for coil cooling options
Cooling mode (and temperature) will depend on the choice of conductor, which depends on the maturity level of the technology and on the timescale of construction
3 TeV machine
Construction in ~15 years
Magnetic fields within Nb3Sn capabilities
Nb3Sn matured, usable
Cooling at 4.5 K – 5.5 K using SC He
Cooling at 4.5 K using He two-phase flow
10 TeV machine
Construction in ~25-30 years
HTS preferred for sustainable collider
Needs development
Cooling at 10 K – 15 K or above
He or H2 possible; in-depth study needed
P. Borges de Sousa

## Slide 50: Evaluation of technology options for Collider Ring magnet cooling
Progress summary
Critical contributors to total heat load deposited on the coil identified
Absorber must operate at or above 250 K (overall cooling effort, distr. losses)
Heat intercept between coil and absorber is a necessity
Electrical power consumption of collider ring cryogenics estimated
Coil must operate at or above 4.5 K
Preliminary evaluation of possible cooling schemes, limitations
With 80K thermal shield between absorber and coil

## Slide 51: Evaluation of technology options for magnet cooling Collider Ring
Needs attention:
Contribution from absorber supports considered disproportionate → effort should be put into the design of an optimized support for the MC absorber conditions
Preliminary cross-section of the coil (and absorber) should be outlined to estimate max. cooling tube size, number, position → allows for some boundaries to cooling scheme layouts
Cooling options for LTS (around 5 K) examined, promising → need R&D to explore the limits of two-phase flow and supercritical cooling in confined geometries
Cooling options for HTS (if 10K+) need in-depth study → He gas cooling does not provide efficient heat transfer; H2 cooling needs demonstration and change of mindset, safety assessment
Cooling of absorber with CO2/water needs in-depth review of the base assumptions, esp. risk-related
Current leads: neither heat loads nor cooling options have been addressed

## Slide 52: Summary
Current effort is inadequate for even the minimal scenario, much less preparation for a demonstration project in a reasonable timeframe.
What is missing now is a dialogue between magnet folks and machine designers. Many trade-offs to explore.
IMCC contends that a 3 TeV Muon Collider could be ready shortly after LHC shutdown in 2041. Technically limited schedule and will need substantial increase in resources on both sides of the Atlantic.
Now we wait for P5 and OHEP

## Slide 53: Muon Collider magnet “catalog”
C
o
m
p
l
e
x
S
e
c
t
o
r
B
a
s
e
l
i
n
e
M
a
g
n
e
t
T
y
p
e
M
a
g
n
e
t
t
e
c
h
n
o
l
o
g
y
F
i
e
l
d
G
r
a
d
i
e
n
t
A
p
e
r
t
u
r
e
G
a
p
W
i
d
t
h
L
e
n
g
t
h
N
u
m
b
e
r
R
a
m
p
t
i
m
e
F
i
e
l
d
r
a
t
e
H
o
m
o
g
e
n
e
i
t
y
P
e
r
s
i
s
t
a
n
c
e
B
e
a
m
p
o
w
e
r
d
e
p
o
s
i
t
i
o
n
C
o
m
m
e
n
t
s
(
T
)
(
T
/
m
)
(
m
m
)
(
m
m
)
(
m
m
)
(
m
)
(
-
)
(
s
)
(
T
/
s
)
/
(
T
/
m
/
s
)
(
u
n
i
t
s
)
(
u
n
i
t
s
/
s
)
(
k
W
/
m
)
T
a
r
g
e
t
a
n
d
C
a
p
t
u
r
e
T
a
r
g
e
t
b
a
s
e
l
i
n
e
s
o
l
e
n
o
i
d
L
T
S
1
5
2
4
0
0
2
1
2
1
6
0
0
0
.
0
0
0
7
1
0
0
1
b
a
s
e
l
i
n
e
1
5
T
,
2
.
4
m
b
o
r
e
d
e
s
i
g
n
,
a
s
s
u
m
e
s
6
h
o
u
r
s
r
a
m
p
-
u
p
t
i
m
e
a
n
d
5
k
W
d
e
p
o
s
i
t
e
d
t
o
t
a
l
p
o
w
e
r
b
a
s
e
l
n
e
s
o
l
e
n
o
i
d
N
C
5
1
5
0
0
.
5
1
1
5
.
0
0
0
0
1
0
0
1
0
0
b
a
s
e
l
i
n
e
5
T
r
e
s
i
s
t
i
v
e
i
n
s
e
r
t
o
p
t
i
o
n
s
o
l
e
n
o
i
d
H
T
S
2
0
6
0
0
1
.
5
1
2
1
6
0
0
0
.
0
0
0
9
1
0
0
0
.
1
5
o
p
t
i
o
n
b
a
s
e
d
o
n
a
H
T
S
c
a
b
l
e
,
r
e
d
u
c
e
d
b
o
r
e
a
n
d
s
h
i
e
l
d
i
n
g
,
o
p
e
r
a
t
i
n
g
a
t
1
0
…
2
0
K
C
a
p
t
u
r
e
a
n
d
d
e
c
a
y
c
h
a
n
n
e
l
s
o
l
e
n
o
i
d
T
B
D
C
o
o
l
i
n
g
I
o
n
i
z
a
t
i
o
n
C
o
o
l
i
n
g
b
a
s
e
l
i
n
e
s
o
l
e
n
o
i
d
T
B
D
2
.
2
6
0
0
2
6
6
2
1
6
0
0
0
.
0
0
0
1
1
0
0
0
.
1
c
e
l
l
A
1
b
a
s
e
l
i
n
e
s
o
l
e
n
o
i
d
T
B
D
3
.
4
5
0
0
1
.
3
2
1
3
0
2
1
6
0
0
0
.
0
0
0
2
1
0
0
0
.
1
c
e
l
l
A
2
b
a
s
e
l
i
n
e
s
o
l
e
n
o
i
d
T
B
D
4
.
8
3
8
0
1
1
0
7
2
1
6
0
0
0
.
0
0
0
2
1
0
0
0
.
1
c
e
l
l
A
3
b
a
s
e
l
i
n
e
s
o
l
e
n
o
i
d
T
B
D
6
2
6
4
0
.
8
8
8
2
1
6
0
0
0
.
0
0
0
3
1
0
0
0
.
1
c
e
l
l
A
4
b
a
s
e
l
i
n
e
s
o
l
e
n
o
i
d
T
B
D
2
.
2
5
6
0
2
.
7
5
2
0
2
1
6
0
0
0
.
0
0
0
1
1
0
0
0
.
1
c
a
l
l
B
1
b
a
s
e
l
i
n
e
s
o
l
e
n
o
i
d
T
B
D
3
.
4
4
8
0
2
3
2
2
1
6
0
0
0
.
0
0
0
2
1
0
0
0
.
1
c
a
l
l
B
2
b
a
s
e
l
i
n
e
s
o
l
e
n
o
i
d
T
B
D
4
.
8
3
6
0
1
.
5
5
4
2
1
6
0
0
0
.
0
0
0
2
1
0
0
0
.
1
c
a
l
l
B
3
b
a
s
e
l
i
n
e
s
o
l
e
n
o
i
d
T
B
D
6
2
8
0
1
.
2
7
5
0
2
1
6
0
0
0
.
0
0
0
3
1
0
0
0
.
1
c
a
l
l
B
4
b
a
s
e
l
i
n
e
s
o
l
e
n
o
i
d
T
B
D
9
.
8
1
8
0
0
.
8
0
6
9
1
2
1
6
0
0
0
.
0
0
0
5
1
0
0
0
.
1
c
a
l
l
B
5
b
a
s
e
l
i
n
e
s
o
l
e
n
o
i
d
T
B
D
1
0
.
5
1
4
4
0
.
8
0
6
7
7
2
1
6
0
0
0
.
0
0
0
5
1
0
0
0
.
1
c
a
l
l
B
6
b
a
s
e
l
i
n
e
s
o
l
e
n
o
i
d
T
B
D
1
2
.
5
9
8
0
.
8
0
6
5
0
2
1
6
0
0
0
.
0
0
0
6
1
0
0
0
.
1
c
a
l
l
B
7
b
a
s
e
l
i
n
e
s
o
l
e
n
o
i
d
T
B
D
1
3
.
6
9
0
0
.
8
0
6
6
1
2
1
6
0
0
0
.
0
0
0
6
1
0
0
0
.
1
c
a
l
l
B
8
F
i
n
a
l
C
o
o
l
i
n
g
b
a
s
e
l
i
n
e
s
o
l
e
n
o
i
d
H
T
S
3
0
5
0
0
.
5
1
7
2
1
6
0
0
0
.
0
0
1
4
0
b
a
s
e
l
i
n
e
d
e
s
i
g
n
f
r
o
m
U
S
-
M
A
P
m
i
n
i
m
a
l
o
p
t
i
o
n
s
o
l
e
n
o
i
d
H
T
S
4
0
6
0
0
.
5
1
7
2
1
6
0
0
0
.
0
0
1
9
1
0
0
0
.
1
0
H
T
S
N
I
o
p
t
i
o
n
,
i
n
c
l
u
d
i
n
g
a
p
e
r
t
u
r
e
m
a
r
g
i
n
t
a
r
g
e
t
o
p
t
i
o
n
s
o
l
e
n
o
i
d
H
T
S
6
0
6
0
0
.
5
1
7
2
1
6
0
0
0
.
0
0
2
8
1
0
0
0
.
1
0
H
T
S
N
I
o
p
t
i
o
n
,
i
n
c
l
u
d
i
n
g
a
p
e
r
t
u
r
e
m
a
r
g
i
n
A
c
c
e
l
e
r
a
t
o
r
R
C
S
1
d
i
p
o
l
e
N
C
1
.
8
3
0
1
0
0
8
.
0
8
4
3
2
7
.
3
5
E
-
0
4
2
4
4
8
.
9
8
0
1
0
R
C
S
2
d
i
p
o
l
e
L
T
S
1
0
1
0
0
2
.
4
2
8
8
1
0
0
0
0
.
0
1
0
1
0
d
i
p
o
l
e
N
C
1
.
8
3
0
1
0
0
6
.
0
6
4
3
2
1
.
8
0
E
-
0
3
1
0
0
0
.
0
0
0
1
0
R
C
S
3
d
i
p
o
l
e
L
T
S
1
0
1
0
0
2
.
6
2
8
8
1
0
0
0
0
.
0
1
0
1
0
d
i
p
o
l
e
N
C
1
.
8
3
0
1
0
0
5
.
0
5
4
3
2
1
.
8
0
E
-
0
3
1
0
0
0
.
0
0
0
1
0
R
C
S
4
d
i
p
o
l
e
L
T
S
1
0
1
0
0
2
.
6
2
8
8
1
0
0
0
0
.
0
1
0
1
0
d
i
p
o
l
e
N
C
1
.
8
3
0
1
0
0
5
.
0
5
4
3
2
8
.
4
6
E
-
0
3
2
1
2
.
7
1
6
1
0
C
o
l
l
i
d
e
r
A
r
c
d
i
p
o
l
e
H
T
S
1
0
3
0
0
1
5
0
1
0
0
0
0
.
0
1
0
1
0
0
.
5
I
R
q
u
a
d
r
u
p
o
l
e
H
T
S
4
6
6
.
3
2
1
7
1
.
4
2
4
1
0
0
0
0
.
0
0
0
1
0
I
Q
F
1
q
u
a
d
r
u
p
o
l
e
H
T
S
3
7
6
.
9
3
2
1
2
.
2
2
4
1
0
0
0
0
.
0
0
0
1
0
I
Q
F
1
a
q
u
a
d
r
u
p
o
l
e
H
T
S
3
0
0
.
7
1
2
6
6
2
4
1
0
0
0
0
.
0
0
0
1
0
I
Q
F
1
b
q
u
a
d
r
u
p
o
l
e
H
T
S
1
9
1
.
4
1
4
1
7
1
3
.
6
4
1
0
0
0
0
.
0
0
0
1
0
I
Q
D
1
q
u
a
d
r
u
p
o
l
e
H
T
S
2
1
4
.
0
3
4
1
1
.
2
5
4
1
0
0
0
0
.
0
0
0
1
0
I
Q
F
2