## Slide 1: A new Test Facility for the Development of High-Field Accelerator Magnets
L. Bottura
TFD review
11/6/2020

## Slide 2: CERN interest in a new facility
After completing testing of EuCARD and EuCARD2 insert magnets (2…3 tests in 2020) the FRESCA2 magnet will become part of a new cable test facility
At this point it will no longer possible to mount HTS inserts of significant size in the magnet bore (anti-cryostat)
The only high-field test facility left for insert testing will be SULTAN at EPFL/SPC
FRESCA2 with integrated Feather.M2 insert and magnetic measurement shaft
Detail of bottom mechanical registration
No HTS R&D without a suitable test bed

## Slide 3: Specification for a new test facility
Approach operating conditions (B, I, T) set as target for the development of future accelerator HTS magnets:
  Bbkg ≈ 15 T
  Iop > 20 kA
  Top ≈ 1.9 K … 100 K
  Large aperture (≈ 150 mm)
A test-bed for HTS inserts (possibly cables, and obviously also relevant to LTS) of different configurations (wound samples, hairpin samples, pressure/temperature controlled samples), targeting peak (total) field of the order of 20 T
These are the HEPdipo specifications

## Slide 4: On the magnet bore
94x144
D=100
D=150

## Slide 5: The additional benefits (to CERN)
Exploit the investment made in the technology developed for block magnets (SMC, RMC, FRESCA2)
Mutualize the effort with the sequence of model magnets planned towards high-field Nb3Sn accelerator magnets of the next generation (the CERN DEMO)
Use this construction as an additional R&D vehicle, to implement and test variants that are deemed appropriate and ready for such realization, and leave a significant heritage

## Slide 6: 1. from FRESCA2 to HEPdipo
FRESCA2
HEPdipo

## Slide 7: 2. relevance to DEMO
 |  | Strands | Dstrand | CU/SC | Width | Thickness
 |  | (-) | (mm) | - | (mm) | (mm)
Option 1: Same width LF and HF | DEMO HF | 44 | 1.10 | 0.8 | 25.700 | 2.002
 | DEMO LF | 56 | 0.85 | 1.2 | 25.700 | 1.547
Option 2: Best width LF and HF | DEMO HF | 44 | 1.10 | 0.8 | 25.958 | 2.002
 | DEMO LF | 56 | 0.85 | 1.2 | 25.475 | 1.547
R= 13.5 mm
R= 34 mm

## Slide 8: HFM – what is it ?
A reinforced, comprehensive R&D programme for superconducting High-Field Magnets, as key technology for future accelerators (hadron colliders, muon colliders, neutrino beams, etc.) and detectors, with great potential for wider societal applications
Budget increased from 2021 to 2024, to reach steady state as of 2026
Covers all SC high-field magnet R&D activities at CERN, including FCC and High-Temperature Superconductors (HTS) under one roof and budget line to maximise synergies
Goals (ambitious) for next ESPP (~2026):
  Nb3Sn: demonstrate technology for large-scale accelerator deployment
  HTS: demonstrate suitability for accelerator magnet applications

## Slide 9
2020
2021
2022
2023
2024
2025
2026
2027
Gate: Evaluate design options for ultimate Nb3Sn performance (16 T)
European Strategy for Particle Physics 2018-2020
European Strategy for Particle Physics 2025-2027
Gate: Demonstrate technology for large scale, ultimate Nb3Sn accelerator magnets
VE dipole
Falcon
RMC-CC
CCT
R2D2-FD
F2D2
SMC, RMC, RMM
DEMO
An Ambitious
LTS Magnet Roadmap
Models and prototypes
Models and prototypes

## Slide 10
2020
2021
2022
2023
2024
2025
2026
2027
Gate: Select options for HTS magnet design
European Strategy for Particle Physics 2018-2020
European Strategy for Particle Physics 2025-2027
Gate: Assess suitability of HTS for accelerator magnets applications
Small coils, HTS tests (Superbend)
An Ambitious
HTS Magnet Roadmap
Small Coils Technology R&D
Eu2 inserts
Insert magnet R&D
Clover leaf
Stand-alone magnet R&D
Eu/Eu2 inserts
HTS magnet R&D
DEMO 20T magnet design
HTS IR quadrupole magnet design
FRESCA2 to Bdg. 163
New high field test station
Conductor R&D (HTS Open Lab ?)