## Slide 1
Mariusz Juchno
US Magnet Development Program
Lawrence Berkeley National Laboratory
US Magnet Development Program
Current status of a shell-based utility structure

## Slide 2: The goal
Shell-based Utility Structure
  Pre-stress for ~17T operation (Nominal 16T, design target 17T)
    Tunable via key shimming
    Peak stress of 180 (?) MPa (150 MPa assembly)
    Requirement on pole separation or tensile stress
  Rapid and reproducible assembly/disassembly
  Compatible with existing 4-layer Cos-theta coil design
  Adjustable to variety of coil designs with minimum modifications
Design limits and sensitivity
  Magnet outer diameter
  Coil design compatibility and combined mechanical/magnetic design
  Sensitivity of mechanical performance
    Dimensions, tolerances, friction, etc.

## Slide 3: Current 4-layer Cos-theta coil

## Slide 4: Magnetic forces vs cable width
Quantities
  Horizontal magnetic force
  Azimuthal stress on the mid-plane based purely on magnetic force accumulation and cable width
Cable width
  15.10 mm (solid line)
  21.13 mm (dashed line)
  Coil ID fixed
    Only radial coil dimensions changed
    Azimuthal coordinates of each block are not changed
    Number of turns not changed
    Bigger coil not optimized
What do we get
  L2 shows higher stress than L1 ?
  High azimuthal stress in L3 ?
  Wider tape seems to reduce stress by <30MPa ?
What we are missing
  Layers impregnated together
  Friction between coils
  Coil deformation and bending
  Horizontal force accumulation
  Structure…

## Slide 5: Forces per block 15.1 mm cable
In the coil L1+L2 block B5 shows highest vertical force and contributes to a high peak stress in block B1
L1+L2 compress L3+L4 against structure and high vertical force in L3+L4 does not deform the coil and stress is not high

## Slide 6: Fixed structure No pre-load
Structure and poles infinitely rigid with fixed displacement
  Not contracting due to cool-down
  Contact with friction
Coil not bonded to the pole
  Not contracting due to cool-down
  Properties for 4.3K
  Layers 1&2 bonded together
  Layers 3&4 bonded together
  Layers 2&3 in contact with friction
Conclusions
  Stress concentration in mid-plane of layer 1
    135 MPa at 15 T
    174 MPa at 17 T
  Stress in layers 2-4 < 90MPa contrary to magnetic analysis estimate
    Bonded coils
    Interaction between layers and structure
135MPa

## Slide 7: Fixed structure, No pre-load Comparison with previous estimation
L1 and L2 potted
  Average stress in 1st block similar to average stress from L1 and L2 magnetic forces
Peak stress ~20MPa higher due to bending
17T shows stress ~30MPa higher than 15T
  Requires ~30MPa more pre-load at CD and MF

## Slide 8: Fixed structure Pre-load for 15 T
Rigid structure
  Shrinkage modeled by contact element offset (-365um)
  Structure does not deform due to MF
Coil and pole shrink during cool-down
Coil can separate from the pole
Horizontal magnetic force: 7 MN/m
Total pole reaction force at cool-down: -8.7 MN/m
Reaction force in each pole at 15T:
  -0.3, -0.8, -1.6, -1.5 MN/m

## Slide 9: Fixed structure Pre-load for 17 T
Rigid structure
  Shrinkage modeled by contact element offset (-385um)
  Structure does not deform due to MF
Coil and pole shrink during cool-down
Coil can separate from the pole
Horizontal magnetic force: 9 MN/m
Total pole reaction force at cool-down: -10.7 MN/m
Reaction force in each pole at 17T:
  -0.2, -0.8, -2.0, -1.6 MN/m

## Slide 10: Exploration of shell parameters
Two types of yoke configurations investigated
  Dipole yokes
  Quad yokes
Shell parameter space
  OD range: 600-800 mm
  TH range: 55-75 mm
Pre-load target
  Pole reaction force 2MN/m higher than magnetic forces
  Adjusted using key shim
Quantities
  Shell and pole reaction forces (RT, CD)
  Shell stress
  Pre-load key shim
  Bladder pressure
    Dipole yokes bladder surface D/2
    Quad yokes bladder surface 0.7D/2

## Slide 11: Dipole yokes Forces, Shell stress
15T
17T
RT key adjusted to the same pre-load after cool-down (2MN/m more than magnetic forces)
Reaction force in the shell equal to the reaction force in the pole

## Slide 12: Dipole yokes Horizontal key, bladder pressure
15T
17T
RT key adjusted required to reach the pre-load
Only half of diameter used for the bladders

## Slide 13: Quad yokes Forces, Shell stress
15T
17T
RT key adjusted to the same pre-load after cool-down (2MN/m more than magnetic forces)
Reaction force in the shell higher due to pre-load locked by the top/bottom yoke

## Slide 14: Quad yokes Horizontal key, bladder pressure
15T
17T
Thicker shim required due to intercepted force
Usable bladder space smaller than in dipole yokes structure

## Slide 15: Summary Other structure types
Dipole yokes
  Sufficient bladder space
  Full reaction force from the shell goes to coil pre-load
  Vertical corner keys increase stress in the structure
  Low number of components
  Adjustment with 2 key types
Quad yokes
  Limited bladder space, bladders less efficient
  Top/bottom yoke limits vertical and intercepts part of the pre-load
  Vertical corner keys increase stress in the structure
  Quad yokes assembly
  Adjustment with 2 key types
Dipole yokes, quad pads
  Sufficient bladder space
  Top/bottom pad limits vertical and intercepts part of the pre-load
  Vertical corner keys increase stress in the structure
  Simple yoke assembly, more components in the coil-pack, bigger OD required
  Adjustment with 2 key types
Dipole yokes, octagonal coil-pack
  Sufficient bladder space, diagonal bladders less efficient but increase total surface
  Full reaction force from the shell goes to coil pre-load
  Force transfer radially, low stress in the structure
  Low number of components
  Adjustment with 3 key types

## Slide 16: Shell based structure – example 1 Dipole yokes
Structure configuration:
  2 yokes (iron)
  2 “collars” (iron)
Shell OD/TH: 610/55 mm
Hor. Mag. forces at 15T: 6.7MN/m
Shell force at CD: 8.7 MN/m
Pole force at CD: 8.7MN/m
Pole force at 15T: 2.0 MN/m

## Slide 17: Shell based structure – example 2 Quad yokes
Structure configuration:
  4 yokes (iron)
  2 “collars” (iron)
Shell OD/TH: 610/55 mm
Hor. Mag. forces at 15T: 6.7MN/m
Shell force at CD: 12.4 MN/m
Pole force at CD: 8.4 MN/m
Pole force at 15T: 2.1 MN/m

## Slide 18: Shell based structure – example 3 Dipole yokes, Quad pads
Structure configuration:
  2 yokes (iron)
  4 pads (iron)
  2 “collars” (iron)
Shell OD/TH: 850/75 mm
Hor. Mag. forces at 15T: 6.9MN/m
Shell force at CD: 12.7 MN/m
Pole force at CD: 8.5 MN/m
Pole force at 15T: 2.3 MN/m

## Slide 19: Shell based structure – example 4 Dipole yokes, Octagon coil-pack
Structure configuration:
  2 yokes (iron)
  2 “collars” (iron)
  Octagon coil-pack
Shell OD/TH: 750/47 mm
Hor. Mag. forces at 15T: 7.0MN/m
Shell force at CD: 8.7 MN/m
Pole force at CD: 8.7 MN/m
Pole force at 15T: 1.7 MN/m

## Slide 20: Structure concept optimized for 16T
Shell OD: 730 mm, TH: 60 mm
Bladder pressure < 45 MPa
Coil stress < 80 MPa @ RT
Structure stress
  < 180 MPa @ RT
  < 360 MPa @ CD & 16 T
17 T with stress ~230 MPa
<2um
4.3 K
16 T
<200MPa
<200MPa

## Slide 21: Conclusions
Integrated magnetic and mechanical design is crucial
  Even simplified mechanical models with fixed OD pre-load can give a good overview of the coil stress limits
Mechanical limitations of the coil design
  Wider cable might not solve the problem for CT
  Stress management in CT coils is an interesting concept
  Optimization of the coil blocks to minimize the peak stress
  Other coil designs
Utility structure
  Minimum OD limited by space available for bladders (~700mm)
  Dipole yoke type structures more efficient
  Structure with octagonal coil-pack
    Compatible with existing CT design (~180 MPa @ 15T after quick optimization)
    Shlomo! Let’s put CCT inside!
  Minimum time for engineering design, procurement and parts fabrication
    6-8 months

## Slide 22: Structure with octagonal coil-pack